## Slide 1
Homomorphic encryption: Cryptography for Cloud computing
Student: Q.D. MCGAW
Supervisors: Dr. Wei Dai and Dr. Cong Ling
Second marker: Professor Athanassios Manikas
20 June 2016

## Slide 2: 1. Objectives of the project
Provide a general purpose C++ API for homomorphic encryption and cloud computing
  This is regularly asked by the cryptographic community
Push current available technologies to their limits
Implement a simple but useful data analysis operation: the average
Prove homomorphic encryption can be used for some computing operations today.

## Slide 3: 2. Cloud computing today
Unsecured communication medium
My sensitive data
My sensitive data
Client side
Cloud storage
l#sd9?/$%fg(45}[
Encryption
l#sd9?/$%fg(45}[
Decryption
l#sd9?/$%fg(45}[
My sensitive data
My sensitive result
Client side
Cloud computing
l#sd9?/$%fg(45}[
Encryption
Decryption
l#sd9?/$%fg(45}[
Decryption
My sensitive data
My sensitive result
^dfsd&12@ff90~
Encryption
^dfsd&12@ff90~
Normal Processing
Ciphertext
Plaintext
Notes: Cloud storage can contain only encrypted data and should not be the main issue here. The main problem is for cloud computing such as amazon elastics cloud computing.
Privacy issues for data on cloud computers. Security issue if cloud computers (priority target for hackers) gets corrupted.

## Slide 4
Homomorphic Encryption
Ciphertext
Plaintext
Unsecured communication medium
My sensitive data
My sensitive result
Client side
Cloud computing
l#sd9?/$%fg(45}[
Encryption
Decryption
l#sd9?/$%fg(45}[
Decryption
My sensitive data
My sensitive result
^dfsd&12@ff90~
Encryption
^dfsd&12@ff90~
Normal Processing
Homomorphic Processing
Homomorphic Decryption
17
100
Xp4#hs11df~9tq?
^dfsd&12@ff90~
Homomorphic Encryption
Homomorphic Decryption
Xp4#hs11df~9tq?
^dfsd&12@ff90~
Homomorphic operations
3. Homomorphic encryption for cloud computing
Notes: Cloud storage can contain only encrypted data and should not be the main issue here. The main problem is for cloud computing such as amazon elastics cloud computing.
Privacy issues for data on cloud computers. Security issue if cloud computers (priority target for hackers) gets corrupted.

## Slide 5: History
Homomorphic encryption has been there for many years, i.e. in the RSA scheme.
Fully homomorphic encryption (FHE) allows arbitrary numbers of additions and multiplications to be processed on ciphertexts in the plaintext space.
It was theoretically proved possible in 2009 by Craig Gentry
This was made practically possible in 2011 by Craig Gentry and Shai Halevi.
Since then many FHE schemes were designed.
There are today several software libraries implementing FHE schemes, such as HElib which is maintained by Shai Halevi (IBM).
Fan and Vercauteren scheme
BGV scheme
LTV scheme
NTRU scheme
GSW scheme
DGHV scheme
DHS sceme
4. The technology today

## Slide 6
Homomorphic ciphertext A
Homomorphic ciphertext B
Homomorphic ciphertext A
Homomorphic ciphertext B
Homomorphic ciphertext A
Homomorphic ciphertext B
Homomorphic ciphertext A
Homomorphic multiplications add more noise to the ciphertext than the homomorphic additions.
The ciphertext can’t be decrypted anymore once the noise grows above a certain threshold.
From now, the number of homomorphic multiplications required is called the complexity
Ciphertext noise
4. The technology today
Notes: Noise is due to randomness added for security purposes

## Slide 7
To counter the growing ciphertext noise, there are two main techniques as listed in the columns of the table below.
Bootstrapping | Levelled homomorphic encryption
Used by Craig Gentry’s first construction (2009) | Used by the BGV scheme (2011)
Homomorphic operations are not bounded. | Homomorphic operations are bounded according to the level parameter L.
Very slow and expensive | More performant, for low values of L.
The level parameter is proportional to the maximum number of homomorphic operations to be performed on a ciphertext.
The smaller L is, the faster the homomorphic operations will be.
Bootstrapping and BGV scheme
4. The technology today

## Slide 8
The library HElib is
  The second most performant homomorphic encryption library
  Portable
  Flexible and tweakable
  Well documented and maintained
It supports
  Bootstrapping, for a fully homomorphic encryption (Craig Gentry’s 2009 construction)
  Modulus key switching, for a levelled homomorphic encryption (BGV scheme)
  Homomorphic addition and multiplication operations in any field.
  SIMD mode, for a higher maximum throughput.
4
17
19
2
Plaintext vector v1
6
2
1
12
Resulting plaintext vector
X
Plaintext vector v2
&f5£sc25@kg*
G3)#fh[2j{\gz5
Encryption
G>7£9sg2/ky0p
Decryption
24
34
19
24
Encryption
Single instruction
Multiple data
The library used: HElib
4. The technology today

## Slide 9: 5. The missing part
There are many schemes and several homomorphic software libraries
There are a few already built applications
  Remote end-to-end voting
  Prince block cipher
  Sorting algorithm
But no general purpose API for number operations such as comparison or division.

## Slide 10
HElib provides only the addition and multiplication homomorphic operations
The only way to design new operations was to use binary – do calculations in the field .
The first step was to implement homomorphic logic gates
The last gate required to go forward was the NOT gate
How does the cloud computer knows what is 1... Without knowing it?
6. Implementation
Starting point

## Slide 11
CLIENT
CLOUD COMPUTER
Generation of key pair
Number of plaintext slots nslots
Creates a vector filled with nslots 1s
Encrypt vector and send SIMD ready ciphertext
Assigns the ciphertext to the “Ones” ciphertext
Copies the “Ones” ciphertext into the “Zeroes” ciphertext
Adds “Zeroes” to “Zeroes”
will be completely different than so the only thing the cloud computer learns is an eventual SIMD result filled with s, which is unlikely to happen due to the high number of plaintext slots (1024).
6. Implementation
The NOT gate

## Slide 12
0
1
………
0
0
0
………
1
0
1
………
1
bits
One number
ciphertexts
6. Implementation
Representation of an n bit number

## Slide 13
Homomorphic Euclidian division arithmetic circuit
bits
bits
bits
Quotient
Binary number A
Binary number B
bits
Remainder
6. Implementation
Example: The homomorphic Euclidean division arithmetic circuit

## Slide 14
AND logic gate
Complexity 1
XOR logic gate
Complexity 0
NOT logic gate
Complexity 0
NAND logic gate
Complexity 1
Requires AND, NOT
OR logic gate
Complexity 1
Requires AND, NOT
NOR logic gate
Complexity 1
Requires AND, NOT
XNOR logic gate
Complexity 0
Requires XOR, NOT
Half Adder
Complexity 1
Requires XOR, AND
Half Subtractor
Complexity 1
Requires XOR, NOT, AND
Half Equal
Complexity 0
Requires XNOR
Lower than comparator
Complexity 1
Requires NOT, AND
2:1 multiplexer
Complexity 3
Requires NAND, NOT
Full Adder
Complexity 3
Requires Half adder, OR
Full Subtractor
Complexity 3
Requires Half subtractor, OR
Full Equal
Complexity 1
Requires Half Equal, AND
Half comparator
Complexity 1
Requires Half Equal, Lower than comparator
Full comparator
Complexity 4
Requires Full Equal, Lower than comparator, AND, OR
Ripple carry adder
Complexity 3n+1
Requires Half and Full Adder
Ripple borrow subtractor
Complexity 3n+1
Requires Half and Full Subtractor
Ripple comparator
Complexity 4(n-1)+1
Requires Half and Full Subtractor
N:1 multiplexer
Complexity 3n
Requires 2:1 multiplexer
Ripple equality tester
Complexity n-1
Requires Half and Full Equality
Binary left & right shift
Complexity 0
Multiplication circuit
Complexity 4-3.5n
Requires Ripple carry adder, left shift and AND
Euclidian division
Complexity +n
Requires Ripple borrow subtractor, shifts, NOT and N:1 multiplexer
Average circuit
Very high complexity
Requires ripple carry adder and Euclidian division
Fast Average circuit
Very high complexity
Requires ripple carry adder and Euclidian division
6. Implementation
The other gates and circuits implemented

## Slide 15
Chart: Level parameter L
| 4 | 10 | 15 | 18 | 20 | 25 | 30 | 50
XOR | 0.97 | 4.68 | 10.32 | 15.6 | 19.84 | 28.1 | 37.5 | 119
AND | 12.06 | 82.35 | 270.16 | 320.3 | 642.04 | 892.2 | 959 | 3172
NOT | 0.94 | 4.53 | 10.47 | 14.1 | 19.83 | 31.2 | 37.5 | 118
NAND | 12.23 | 83.75 | 272.5 | 323.4 | 645.95 | 909.4 | 967 | 3185
OR | 12.81 | 85.31 | 277.18 | 331.3 | 643.26 | 917.2 | 998 | 3180
NOR | 12.55 | 84.53 | 276.57 | 331.2 | 642.58 | 900 | 984 | 3165
XNOR | 0.94 | 4.53 | 10.62 | 15.6 | 19.76 | 31.3 | 37.5 | 120
Chart: Level parameter L
| 4 | 10 | 15 | 18 | 20 | 25 | 30 | 50
M/A ratio | 13.0658 | 18.3373 | 26.1798 | 21.6258 | 32.4814 | 29.957 | 26.0533 | 26.6849
Homomorphic multiplications add between 12 and 34 times more noise than the homomorphic addition.
This is why it is called complexity here.
7. Results and evaluations
Logic gates

## Slide 16
Chart: Time for 1024 SIMD operations, in milliseconds
| Half Adder | Full Adder | Half Subtractor | Full Subtractor | Half equality comparator | Full equality comparator | Lower Than comparator | Half comparator | Full comparator | Multiplexer 2:1
Time in ms | 281 | 1016 | 281 | 991 | 0 | 297 | 281 | 297 | 1297 | 1000
Chart: Complexity for combinational circuits
| Half Adder | Full Adder | Half Subtractor | Full Subtractor | Half equality comparator | Full equality comparator | Lower Than comparator | Half comparator | Full comparator | Multiplexer 2:1
 | 1 | 3 | 1 | 3 | 0 | 1 | 1 | 1 | 4 | 3
7. Results and evaluations
Combinational circuits, for 1024 SIMD plaintext slots
The complexity of a homomorphic circuit and its execution time are highly correlated

## Slide 17
Chart: Number of bits n
Ripple Comparator | 1 | 5 | 9 | 13 | 17 | 21 | 25 | 29 | 33 | 37 | 41 | 45 | 49 | 53 | 57 | 61
Ripple Carry adder | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 28 | 31 | 34 | 37 | 40 | 43 | 46 | 49
Ripple Borrow subtractor | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 28 | 31 | 34 | 37 | 40 | 43 | 46 | 49
Multiplexer n:1 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45 | 48
Ripple equality tester | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Right/Left shift | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LINEAR
Chart: Total time and time per operation vs Complexity
| 7 | 10 | 13 | 16 | 19 | 22 | 25
Overall time (seconds) - 1024 slots | 1.828 | 3.235 | 5.016 | 6.984 | 10.453 | 14.125 | 17.875
Time per operation (milliseconds) - 1024 slots | 1.7852 | 3.1592 | 4.8984 | 6.8203 | 10.208 | 13.7939 | 17.4561
Overall time (seconds) - 1800 slots | 2.281 | 3.922 | 6.265 | 11 | 14.281 | 17.953 | 23.063
Time per operation (milliseconds) - 1800 slots | 1.2672 | 2.1789 | 3.4806 | 6.1111 | 7.9339 | 9.9739 | 12.8128
Increasing the number of SIMD data slots decreases the time per operation
7. Results and evaluations
Sequential circuits, for 1024 SIMD plaintext slots

## Slide 18
This involves the following 5 circuits built on top of the sequential circuits:
  Binary multiplication
  Binary Euclidean division
  Binary Average
  Binary “Fast” Average which only calculates the quotient of a division
Chart: Complexity vs Number of bits
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Complexity Multiplication | 1 | 11 | 30 | 58 | 95 | 141 | 196 | 260
Complexity Euclidian division | 7 | 26 | 57 | 100 | 155 | 222 | 301 | 392
Exponential
7. Results and evaluations
Arithmetic circuits, for 1024 SIMD plaintext slots
Arithmetic circuits become quickly unusable as the number of bits n grows

## Slide 19
Chart: Minimum level parameter for arithmetic circuits for different n
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Ripple carry adder | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 28
Multiplication circuit | 8 | 13 | 17 | 22 | 28 | 32 | 37 | 41
Euclidean division circuit | 11 | 21 | 50 | 55
Average circuit N=2 | 25 | 45
Fast average circuit, N=4 | 11 | 13 | 15 | 17 | 19 | 21 | 26 | 28
Chart: Time per operation (ms) vs Number of bits n
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Ripple carry adder | 1.7852 | 3.1592 | 4.8984 | 6.8203 | 10.208 | 13.7939 | 17.4561 | 20.8594
Multiplication circuit | 4.2314 | 16.1738 | 48.8428 | 91.248 | 127.3694 | 185.8683 | 311.12 | 974.5525
Euclidean division circuit | 10.9258 | 45.5781 | 280.8607 | 474.8179
Average circuit N=2 | 61.3857 | 496.8711
Fast average circuit, N=4 | 11.9014 | 18.3105 | 27.2979 | 37.1553 | 49.0566 | 57.8457 | 78.9811 | 101.0672
Not timely useful anymore
7. Results and evaluations
Arithmetic circuits, for 1024 SIMD plaintext slots

## Slide 20: 8. Conclusion
Some operations can be used now with the API developed and are not too expensive in terms of time.
  Binary additions, subtractions, comparisons
  Binary “Fast” averages (based on shifts)
  Binary multiplications, for numbers up to 8 bits.
  Multiplexers
Code is
  Robust: 75% of the API code is covered by unit tests
  Open source: http://qdm12.github.io/hbc/ and well documented
  Easy to setup and use: A makefile was crafted for Windows and Linux to download, compile and install everything
  Compatible: On all platforms, although some like OSX will have to install manually.
A lot of future work possible
  Changing the sequential and arithmetic circuits algorithms
  Adding more homomorphic circuits
  Using bootstrapping for very complex circuits
  Adding parallel circuits for an even bigger throughput
  Using multiple cores of the CPU, or even GPU with the cuHE library
Already used by a Computer science Masters student in the University of Manitoba, Canada.
9. Thank you
10. Questions
11. Answers

## Slide 23
A: 101
B: 010
X: 000 101
X: 001 010
R: 001 – 010 = 1111
X: 001 010
Left shift
Left shift
Iteration 1
X: 010 100
R: 010 – 010 = 0000
X: 000 100
Left shift
Iteration 2
X: 001 001
R: 001 – 010 = 1111
X: 001 001
Left shift
Iteration 3
X: 010 010
Q: 010
R: 010
Right shift
R: 001
Q: 010
LOOP
5 / 3 ?
5 = 2 x 2 + 1
Blue arrows operations represent memory operations or shifts and have a zero homomorphic complexity
Red and orange arrows have a high homomorphic complexity
The green arrow is a NOT gate (zero complexity)

## Slide 24
0
OR
&f5£s@kg*
Encryption
1
………
0
0
0
………
1
a39es$sfz
Encryption
G6”15fl8h
0
1
………
1
Decryption